## Slide 2
FixationCross.pptx — Thaler ABC optimal fixation target
Design reference:
Thaler, Schütz, Goodale & Gegenfurtner (2013). What is the best fixation target? The effect of target shape on stability of fixational eye movements. Vision Research 76:31–42.
Display geometry (Pitt BOLDscreen):
Viewing distance: 139.0 cm
Screen size: 69.84 × 39.29 cm
Native resolution: 1920 × 1080 px
Field of view: 28.20° × 16.09°
Scale: 68.07 px/° (146.9 µm/px on screen)
Target parameters:
Outer disk diameter: 1.2° (81.7 px, 2.97 cm)
Inner disk diameter: 0.4° (27.2 px)
Crosshair thickness: 0.2° (13.6 px)
Foreground: RGB(0, 0, 0) (black)
Background: RGB(128, 128, 128) (mid-gray, iso-luminant with typical task stimuli)
Usage notes:
• Present full-screen on the BOLDscreen. Slide is authored at exactly 1920 × 1080 px (6350 EMU/px) so PowerPoint coordinates map 1:1 to display pixels — no rescaling.
• Visual angles assume 139 cm viewing distance. If a participant's head is unusually small/large, recompute px/° before publishing.
• For PsychoPy usage, prefer drawing the target programmatically with deg units (see scripts/generate_fixation_cross.py) rather than importing this .pptx as an image.